## Slide 1
EOCap4Africa 1 How to conduct a Remote Sensing case study
c) Importance of field (in situ) data in Remote Sensing

## Slide 2
Learning objectives
Define in situ (field) data and its role in remote sensing
Understand why ground data is essential for validation and accuracy
Identify different types of in situ data used in case studies
Recognise challenges and best practices for integrating field data

## Slide 3
What is in situ data
Definition
Field data collected directly from the ground to provide real-world reference points
Used to validate, calibrate, and enhance remote sensing analysis
Why is it important?
Remote sensing provides indirect measurements (e.g., NDVI for vegetation health)
Field data confirms what is really happening on the ground
(Alkindi 2022)

## Slide 4
The Role of in situ data in remote sensing
Why remote sensing data alone is not sufficient for your RS* case study
Atmospheric effects, sensor limitations, and data resolution can introduce errors
Ground truthing helps improve classification accuracy
Allows correlation between spectral values and real-world conditions
How in situ data will enhance the value of your RS case study
Step 1: Collect satellite data (e.g., Sentinel-2)
Step 2: Identify study areas requiring ground validation
Step 3: Conduct field surveys, record data, and take GPS-tagged photos
Step 4: Compare field measurements with remote sensing results
*RS = Remote Sensing

## Slide 5
Types of in situ data
Which types of In-Situ data can you think of?
(Zhang et al. 2022)

## Slide 6
Types of in situ data
Purpose: Improve analysis of agricultural and hydrological studies
Example: Ground sensors measuring soil moisture vs. satellite estimates
Vegetation & land cover surveys
Purpose: Validate land classification (forest, agriculture, wetlands)
Example: Using squares to measure tree canopy density
Water quality sampling
Soil & moisture measurements
Purpose: Validate satellite-based water turbidity, algae, and pollution levels
Example: Taking pH and chlorophyll samples for lake monitoring

## Slide 7
Types of in situ data
  Purpose: Provide high-resolution reference images for validating satellite classifications
  Example: Drones capturing ultra-high-resolution imagery of deforestation sites
Climate & weather data
  Purpose: Provide real-time atmospheric corrections for satellite data
  Example: Temperature, humidity, and wind speed logs from weather stations
GPS & drone surveys

## Slide 8
Combining in situ and satellite data
(Morales-Hidalgo et al. 2017)

## Slide 9
Challenges in collecting and using in situ data
Time-consuming & expensive
  Requires field teams, specialized equipment, and travel costs.
Data collection errors
  Inconsistent sampling methods can introduce biases.
Scalability issues
  Field surveys cover limited areas, whereas satellites provide regional/global coverage
Weather & environmental barriers
  Remote areas, harsh terrain, and seasonal access limitations

## Slide 10
Best practices for using in situ data
Use standardized protocols
Follow global methodologies for data collection (e.g., FAO Land Cover Classification)
Ensure spatial alignment
Match field data coordinates with satellite imagery
Automate data collection
Use GPS, sensors, and mobile apps for accuracy
Combine multiple data sources
Improve validation by integrating drone imagery, government datasets, and historical records
  Document metadata
  Record who collected data, when, and under what conditions

## Slide 11
Choose in situ data for your own case study
Within the next 20 minutes:
Think of at least three types of in situ data you can use to make your case study better!
Go outside, take your phone with you, and do some in-situ sampling (GPS tagged pictures, Quick Capture [needs to be prepared by supervisor])

## Slide 12
In situ data is essential for validating remote sensing analysis
Ground truthing improves classification accuracy and interpretation
Challenges include cost, errors, and limited coverage, but best practices help improve reliability
Summary & key Takeaways

## Slide 13
Sources
Alkindi, K. M. (2022, February 1). The use of remote sensing will be a boon for farmers. UNESCO Chair on Aflaj Studies. Retrieved February 10, 2025, from https://ishraqa.unizwa.edu.om/article_170504.html
Morales-Hidalgo, D., Kleinn, C., & Scott, C. T. (2017). Voluntary guidelines on national forest monitoring. Food and Agriculture Organization of the United Nations. ISBN 978-92-5-109619-2.
Zhang, Y., Yang, Y., Zhang, Q., Wang, X., & Others. (2022). Toward multi-stage phenotyping of soybean with multimodal UAV sensor data: A comparison of machine learning approaches for leaf area index estimation. Remote Sensing, 15(1), 7. https://doi.org/10.3390/rs15010007

## Slide 14: Thank you for your attention!
Dr. Insa Otte, Hanna Schulten
(on behalf of the EOCap4Africa Team)
and colleagues
insa.otte@uni-wuerzburg.de