## Slide 1
EOCap4Africa 3 Overview of available Spatial Data and respective Sources
a) Sentinel 2 Images - Spectral, temporal and spatial resolution

## Slide 2
Learning objectives
Explain what Sentinel-2 is and its role in Earth observation
Define spectral, temporal, and spatial resolution in remote sensing
Understand how Sentinel-2’s resolution impacts different applications
Identify the strengths and trade-offs of Sentinel-2 data

## Slide 3
What is Sentinel-2
Sentinel-2 is part of the European Space Agency's (ESA) Copernicus Program, designed for land monitoring applications
The mission consists of two satellites (Sentinel-2A & Sentinel-2B) working together to provide frequent, high-resolution imagery
(ESA 2015)

## Slide 4
Sentinel-2 twin configuration
Why two satellites?
Improves temporal resolution – Each satellite orbits 180° apart, covering the same location every 5 days (instead of 10 days with one satellite)
Ensures mission continuity – If one satellite fails, the other continues operations
Enhances global coverage – Together, they provide complete Earth coverage at high frequency
Orbits & positioning:
Sentinel-2A launched on June 23, 2015
Sentinel-2B launched on March 7, 2017
Both operate in sun-synchronous orbits at
786 km altitude
(Copernicus n.d.)

## Slide 5
Key applications of Sentinel-2
Vegetation monitoring (e.g., crop health, deforestation)
Land use & land cover mapping
Water resource monitoring
Disaster response (wildfires, floods, droughts)

## Slide 6
Temporal resolution
  The frequency of satellite revisits over the same area
What is temporal resolution
Why temporal resolution matters
  Enables time-series analysis (E.g., monitoring seasonal vegetation cycles)
  Allows change detection (E.g., wildfire burn area before/after an event)
Sentinel-2 temporal resolution
  5-day revisit time (when both Sentinel-2A and Sentinel-2B are operational)
  Frequent coverage makes it ideal for monitoring rapid changes (e.g., agriculture, disasters, deforestation)

## Slide 7
Spectral resolution
  The ability of a satellite to capture information in different wavelengths of the electromagnetic spectrum
What is spectral resolution
Why spectral resolution matters
  Different wavelengths allow differentiation between land cover types
  Enables vegetation indices (e.g., NDVI, EVI) for monitoring crop health and forest conditions

## Slide 8
Spectral resolution of Sentinel-2
(Freie Universität Berlin n.d.)

## Slide 9
Spectral resolution of Sentinel-2
(Freie Universität Berlin n.d.)

## Slide 10
Spatial resolution
  Describes the pixel size in Raster data
  Eg. the size of the smallest object that can be detected in an image
What is spatial resolution
Sentinel-2 spatial resolution
  10m resolution: Visible and NIR bands (detailed vegetation and urban analysis)
  20m resolution: Red Edge, SWIR (biophysical parameters like water content, biomass)
  60m resolution: Atmospheric bands (used for corrections, not surface analysis)

## Slide 11
Spatial resolution of Sentinel-2
(ESA 2022)
Image of Kilimanjaro highlighting the spatial resolution

## Slide 12
Hands-On: Sentinel-2 bands
Spectral indices with Sentinel-2
  Let’s get started:
  Name all bands with a 20m resolution of Sentinel-2
  Name all bands with a 60m resolution of Sentinel-2
Rebuild the following index equations with Sentinel-2 bands
  NDVI
  EVI
  NDWI
  NBR

## Slide 13
Sentinel-2 has 13 spectral bands, allowing detailed vegetation, water, and land monitoring
10m, 20m, and 60m spatial resolutions balance high detail with wide coverage
5-day temporal resolution makes it ideal for tracking changes over time
Different resolutions serve different applications, from agriculture to disaster management
Summary & key takeaways

## Slide 14
Sources
Copernicus. (n.d.). Sentinel-2 mission overview. Retrieved February 10, 2025, from https://sentiwiki.copernicus.eu/web/s2-mission
European Space Agency (ESA). (2022, September 15). A snowy Kilimanjaro - ESA-Sentinel-2-L1C-Image [Satellite image]. Retrieved February 10, 2025
European Space Agency (ESA). (2015, June 11). Sentinel-2 hat die Erdoberfläche im Blick. Retrieved February 10, 2025, from https://www.esa.int/Space_in_Member_States/Germany/Sentinel-2_hat_die_Erdoberflaeche_im_Blick
Freie Universität Berlin. (n.d.). Sentinel-2. Retrieved February 10, 2025, from https://blogs.fu-berlin.de/reseda/sentinel-2/

## Slide 15: Thank you for your attention!
Dr. Insa Otte, Hanna Schulten
(on behalf of the EOCap4Africa Team)
and colleagues
insa.otte@uni-wuerzburg.de