## Slide 1
EOCap4Africa 3 Overview of available Spatial Data and respective Sources
b) Sentinel 2 images - Possibilities and Limitations

## Slide 2
Learning objectives
Identify the main strengths and applications of Sentinel-2 data
Understand the limitations of Sentinel-2 and how to address them
Make informed choices when selecting Sentinel-2 for remote sensing projects

## Slide 3
What makes Sentinel-2 great?
  10m, 20m, and 60m spatial resolution allows detailed environmental and land use analysis.
Global land monitoring at high resolution
Frequent revisit times
5-day temporal resolution (with Sentinel-2A and 2B working together)
Ideal for tracking seasonal changes, deforestation, and agricultural cycles
Rich spectral information
13 bands covering Visible, Near-Infrared (NIR), and Shortwave Infrared (SWIR)
Enables advanced analysis like NDVI (vegetation health) and water turbidity monitoring

## Slide 4
What makes Sentinel-2 great?
Sentinel-2 Data is publicly available and free
Copernicus Data Space Ecosystem (ESA Official Source)
https://dataspace.copernicus.eu/
Direct download of raw Sentinel-2 imagery (Level-1C and Level-2A)
Google Earth Engine (Cloud Processing & Analysis)
https://earthengine.google.com/
Provides pre-processed Sentinel-2 data for easy analysis
Sentinel Hub EO Browser (Quick Visualization & Download)
https://www.sentinel-hub.com/explore/eobrowser/
View and analyze Sentinel-2 imagery without downloading large files.
And many more …

## Slide 5
Strength and uses of Sentinel-2
For each of Sentinel-2s strength, think of why it matters and what potential use cases could be!
Feature | Why It’s Useful | Example Use Case
High-resolution (10m for visible bands) | Allows detection of small-scale land changes | 
Frequent revisit times (5 days) | Enables time-series analysis | 
Multi-spectral bands (13 bands) | Allows vegetation, water, and land use analysis | 
Cloud-free composites possible | Data from multiple dates can be merged to remove clouds | 
Free and open-source data | Accessible to researchers, governments, and NGOs | 
Within the next 15 - 20 min, find at least one scientific paper for each feature and put the reference in the table and present your results to the class

## Slide 6
Strength and uses of Sentinel-2
Your solution could look like this:
Feature | Why It’s Useful | Example Use Case
High-resolution (10m for visible bands) | Allows detection of small-scale land changes | Mapping farmland boundaries, urban expansion
Frequent revisit times (5 days) | Enables time-series analysis | Monitoring crop growth, seasonal vegetation cycles
Multi-spectral bands (13 bands) | Allows vegetation, water, and land use analysis | NDVI for plant health, SWIR for soil moisture
Cloud-free composites possible | Data from multiple dates can be merged to remove clouds | Generating annual cloud-free mosaics
Free and open-source data | Accessible to researchers, governments, and NGOs | Environmental monitoring, conservation efforts

## Slide 7
Limitations of Sentinel-2
Sentinel-2 cannot see through clouds
  Sentinel-2 is an optical sensor
  → Cannot capture data during heavy cloud cover, study site is not fully visible
  Workaround: Use multi-date composites or combine with Sentinel-1 (SAR-based)
(Fjord 2022)

## Slide 8
Limitations of Sentinel-2
Limited nighttime or low-light data
  Sentinel-2 does not have thermal sensors and is not a radar satellite
  → Cannot be used for nighttime monitoring
  Workaround: Use Landsat 8 (thermal bands) or
  MODIS for continuous global coverage
(Landsat Missions 2022)

## Slide 9
Limitations of Sentinel-2
Moderate spatial resolution
  10m resolution is good, but not as high as commercial satellites
  e.g., PlanetScope at 3m, Pleiades 1A/B satellites at 0.5m, WorldView at 0.3m
(Kowaleczko et al. 2013)

## Slide 10
Limitations of Sentinel-2
Data storage and processing requirements
  Large file sizes (especially raw Level-1 products)
  Workaround: Use cloud-based processing (Google Earth Engine, Sentinel Hub)
Limited to land monitoring
  Cannot capture deep-sea ocean data (e.g., bathymetry, deepwater studies)
  Workaround: Use Sentinel-3 for oceanographic applications

## Slide 11
Sentinel-2 vs. other satellites
When to use which satellite?
Satellite | Best For | Why?
Sentinel-2 | General land cover, agriculture, vegetation, water monitoring | High spectral & spatial resolution, free access
Sentinel-1 | Cloudy areas, radar applications | Uses SAR (Synthetic Aperture Radar) to penetrate clouds
Landsat 4 - 9 | Long-term land cover change, urban studies | 30m resolution but with decades of historical data
MODIS | Large-scale monitoring, global vegetation trends | Daily images but lower spatial resolution
Commercial satellites (PlanetScope, WorldView) | High-resolution urban mapping, small-scale change detection | 3m–0.3m resolution but expensive

## Slide 12
Hands-On: Sentinel-2 bands
Getting data
Let’s get started:
  https://browser.dataspace.copernicus.eu/
  Follow the link above to register and login to Copernicus Data Space
  Download any area of your interest
Hint: Simply select the “Search” tab in the GUI, enter your search terms, choose the location and time, and from the list of data products, you can download your selection by clicking on the “download” icon.

## Slide 13
Optional hands-on task
Let’s get started with Landsat:
  https://glovis.usgs.gov/app or https://earthexplorer.usgs.gov/
  Follow the link above to register and login to USGS website
  Explore and download any area of your interest
Hint: Use this tutorial link to assist you in downloading Landsat and DEM data https://www.youtube.com/watch?v=42YTGa_k9ys
Other Resources: https://www.earthdatascience.org/courses/use-data-open-source-python/multispectral-remote-sensing/modis-data-in-python/download-modis-hdf4-data/ (MODIS data access

## Slide 14
Sentinel-2 is powerful for land monitoring, with great spectral, spatial, and temporal resolution
It has limitations in cloud cover, resolution, and thermal/nighttime imaging
Understanding when and how to use Sentinel-2 improves analysis accuracy
Combining Sentinel-2 with other satellite data helps overcome its weaknesses
Different resolutions serve different applications, from agriculture to disaster management
Summary & key takeaways

## Slide 15
Sources
Fjord, M. (2022, April 1). Cloudless synthetic Sentinel-2 data. ClearSKY Vision. Retrieved February 10, 2025, from https://clearskyvision.medium.com/cloudless-synthetic-sentinel-2-data-49ddcab3c953
Landsat Missions. (2020, January 15). Nighttime Landsat 8 image of the Taal Volcano [Satellite image]
Kowaleczko, P., Tarasiewicz, T., Ziaja, M., Kostrzewa, D., Nalepa, J., Rokita, P., & Kawulok, M. (2023). A real-world benchmark for Sentinel-2 multi-image super-resolution. Scientific Data, 10, Article 644 https://doi.org/10.1038/s41597-023-02439-4
U.S. Geological Survey. Retrieved February 10, 2025, from https://www.usgs.gov/media/images/nighttime-landsat-8-image-taal-volcano

## Slide 16: Thank you for your attention!
Dr. Insa Otte, Hanna Schulten
(on behalf of the EOCap4Africa Team)
and colleagues
insa.otte@uni-wuerzburg.de