## Slide 1
EOCap4Africa 5 Introduction to R and QGIS
b) Introduction to QGIS

## Slide 2
Learning objectives
Understand the general layout of QGIS
Identify key toolbars and panels in the interface
Learn the basics of coordinate reference systems (CRS) and projections
Install and activate essential QGIS plugins

## Slide 3
Starting QGIS for the first time
Start your QGIS application
Open a new project on the left
Old projects will appear on the right

## Slide 4
Menu bar
Map view
see your data visualised here
Browser panel
Layer panel
geodata itself is here
Status bar
Toolbars

## Slide 5
Understanding the QGIS layout
Section | Function | Key Features
Menu bar | Access all functions | File, edit, view, layer, plugins
Toolbars | Quick access to tools | Add layers, zoom, measure, select features
Layers panel | Manage map layers | Turn layers on/off, reorder them
Browser panel | Find and add data | Connect to files, databases, online services
Map canvas | Display your map | Shows layers in the project
Status bar | Coordinates & scale | Shows CRS, rendering progress

## Slide 6
Viewing data in QGIS
Type world in the coordinate field in the status bar to access a vector world map!

## Slide 7
Viewing data in QGIS
Try it out for yourself!
What has changed in your QGIS after the data was added?
Zoom around the map and find where you are currently located.

## Slide 8
Understanding projections and CRS
What is a CRS?
A Coordinate Reference System (CRS) defines how spatial data is positioned on the earth's surface
Every GIS dataset has a specified projection and datum that determine how it is displayed on a map
Incorrect CRS settings can lead to misaligned or distorted maps
Key Components of a CRS:
Datum: Defines the reference model of the earth's shape (e.g., WGS84, NAD83)
Projection: A mathematical transformation that flattens the 3D Earth onto a 2D plane
Coordinate system: Defines the measurement units (e.g., latitude/longitude, meters)

## Slide 9
Understanding projections and CRS
(Minn 2024)

## Slide 10
Why the CRS matters
Problem | Cause | Solution
Misaligned layers | Different CRS in datasets | Convert to a common CRS
Distorted shapes | Using an unsuitable projection | Choose a projection suitable for the region
Incorrect measurements | Mixing projected and unprojected data | Ensure all layers use a projected CRS
Affects: Accuracy of spatial analysis (distance, area, angles) Alignment of datasets (combining multiple sources) Correct display on maps (avoiding distortions)

## Slide 11
Common CRS
Projection name | Type | Best used for | EPSG Code
WGS84 | Geographic | Global datasets, GPS | EPSG:4326
UTM Zones | Projected | Local/regional precision mapping | EPSG:326XX
Web Mercator | Projected | Web-based maps (Google Maps, OpenStreetMap) | EPSG:3857
Albers Equal Area | Projected | Large-scale national maps | EPSG:5070
Africa Albers Equal Area Conic | Projected | Africa-focused data | EPSG:102022

## Slide 12
Changing the CRS in QGIS
You can check the EPSG code in the status bar on the right

## Slide 13
Changing the CRS in QGIS
Changing the CRS of a project
Go to Project in the menu bar → properties → CRS
Select a new projection (e.g., EPSG:4326 for global datasets)
Reprojecting a layer
Select Layer in layer panel by right clicking → Export → Save As…
Choose the desired CRS from the dropdown list
Save the reprojected layer as a new file

## Slide 14
Tasks
Try it out for yourself and reproject your data!
Describe the changes!
For which study would you use which CRS?

## Slide 15
Installing and managing plugins
Why Use plugins?
Extend QGIS functionality (e.g., web mapping, data analysis, automation)
How to install a plugin:
Go to plugins in the menu bar → Manage and install plugins
Search for the desired plugin
Click install and enable it

## Slide 16
Installing and managing plugins
Lets install your first plugin!
Search for QuickMapServices

## Slide 17
Installing and managing plugins
Once you have found it, the option to install it will show up on the bottom right
Installed packages show up on the installed page
Make sure that QuickMapServices and Processing both have their box ticked!

## Slide 18
Using QuickMapServices
Web -> QuickMapServices -> OSM -> OSM Standard lets you add a map to the background

## Slide 19
Task
Explore the OpenStreetMap!

## Slide 20
Saving a QGIS project
Why Save your project?
QGIS projects store layer arrangements, styles, and settings, allowing you to continue working without reloading everything
Prevents losing progress when handling multiple datasets
How to Save a QGIS project:
Go to Project → Save As…
Choose a location and enter a meaningful filename (e.g., land_cover_analysis.qgz)
Click Save to store the project

## Slide 21
Task
Save your project!

## Slide 22
QGIS has an intuitive layout with key panels: Layers, browser, and map canvas
Coordinate reference systems (CRS) determine how spatial data aligns on earth, and using the correct projection is crucial for accuracy
Common projections include WGS84 (global), UTM (local), Web Mercator (web mapping), and Africa Albers Equal Area Conic (for African studies)
Plugins enhance QGIS capabilities—OpenLayers, QuickMapServices, and GRASS GIS are useful additions
Saving your QGIS project regularly ensures you don’t lose progress and maintains organized workflows
Summary & key takeaways

## Slide 23
Sources
Minn, M. (2024, October 27). Map projections. Retrieved February 10, 2025, from https://michaelminn.net/tutorials/gis-projections/

## Slide 24: Thank you for your attention!
Dr. Insa Otte, Hanna Schulten
(on behalf of the EOCap4Africa Team)
and colleagues
insa.otte@uni-wuerzburg.de