## Slide 1
EOCap4Africa Excursion
In-situ sampling in QField

## Slide 2
Learning objectives
Configure QGIS projects for mobile field data collection.
Set up attribute forms with proper field types and constraints.
Deploy projects to QField using both cloud and offline methods.
Collect spatial data with photos and GPS coordinates in the field.
Synchronize field-collected data back to QGIS desktop.

## Slide 3
What is QField?
Open-source mobile application for Android and iOS
Enables editing QGIS projects on mobile devices
Takes QGIS projects into the field for effective data collection
Maintains QGIS styling and edit widgets
(opengisch n.d.)

## Slide 4
QField workflow
Configure QGIS project (desktop)
2. Set up data layers and attributes
3. Deploy to QField
4. Collect data in the field
5. Synchronise back to QGIS

## Slide 5
Configuring the QGIS project
Folder structure:
  Project Folder
    Your QGIS project
    “ExportQField”
    “ImportQField”
Save project without spaces in filename
Create the project

## Slide 6
Configuring the QGIS project
Under the browser (top left) you will find the dropdown XYZ Tiles
Use the OpenStreetMap basemap
In QGIS: Basemap

## Slide 7
Configuring the QGIS project
QGIS plugin: OSM Place Search
  Allows you to browse through the different place features available in the OpenStreetMap data
Under Plugins in the Menu toolbar, click Manage and Install Plugins
In the search bar, type OSM Place Search and install the plugin
A new window should appear in the side panel where you can enter your AOI
Area of Interest (AOI)

## Slide 8
Creating the GeoPackage
A file-based database where you can store multiple layers, including points, lines, polygons, and raster data
Datasets are saved in one file, instead of multiple (shapefiles)
Ends in .gpkg
What is a GeoPackage?

## Slide 9
Creating the GeoPackage
Create a GeoPackage
Select Layer > Create Layer > New Geopackage Layer:
  For Database, click on (…) and select your project folder and give a suitable name
  Choose a Table name
  For Geometry type, select points
  Select the desired Coordinate Reference System (CRS) by clicking on the Globe icon

## Slide 10
Creating the GeoPackage
Create a GeoPackage
Under New Field add the following attribute columns:
  lulc_class: Value Map widget with predefined options (Text)
  Date: Auto-populated with now(), non-editable (Date and time)
  Photo: Attachment widget with relative paths and document viewer (Text)
  Latitude/Longitude: Auto-populated ($x, $y), non-editable (Decimal)

## Slide 11
Creating the GeoPackage
Create a GeoPackage
Under New Field add the following attribute columns:
  lulc_class: Value Map widget with predefined options (Text)
  Date: Auto-populated with now(), non-editable (Date and time)
  Photo: Attachment widget with relative paths and document viewer (Text)
  Latitude/Longitude: Auto-populated ($x, $y), non-editable (Decimal)

## Slide 12
Creating the GeoPackage
Create a GeoPackage
Under New Field add the following attribute columns:
  lulc_class: Value Map widget with predefined options (Text)
  Date: Auto-populated with now(), non-editable (Date and time)
  Photo: Attachment widget with relative paths and document viewer (Text)
  Latitude/Longitude: Auto-populated ($x, $y), non-editable (Decimal)

## Slide 13
Attribute configuration
Edit file properties
Go the sample layer: Layer Properties > Attribute Form
Select Drag and Drop Designer from the dropdown
  Do not need to edit the fid field. QGIS creates this for every GeoPackage by default
Remove the fid field from the visible fields by pressing the -

## Slide 14
Attribute configuration
LULC_class
Select lulc_class:
  Change the Widget type from Text edit to Value Map
  Enter the Value and Description for your lulc classes
  Check the Not null button under the Constraint
  Click Apply

## Slide 15
Attribute configuration
Date
Select date:
  Make sure it has the Date/Time format under the Widget Type
  Under General, uncheck Editable
  Under Defaults, in the Default value type, use now()
  Click Apply

## Slide 16
Attribute configuration
Photo
Select photo:
  In the Widget Type section, select Attachment
  Check Relative paths and select Relative to Project Path
  Check the ‘Use a hyperlink for document path” box
  Select Image for the Type
  Set Width and Height to 400px and 300px
  Click Apply

## Slide 17
Attribute configuration
Latitude and Longitude
Edit latitude and longitude:
  Under General, uncheck Editable.
  In the Default value bar, type in $x for latitude and $y for longitude

## Slide 18
QField synchronisation methods
QField cloud
Two methods:
QField offline

## Slide 19
QField synchronisation methods
Cloud method | Offline method
Automatic synchronisation | Functions almost completely without Wi-Fi
Multiple users can work on the same project | Requires multiple manual steps (eg. USB transfer)
Easier setup | More complex
Best for: most cases, teams, projects with many changes | Best for: extremely remote studies, sensitive data

## Slide 20
QField cloud
In QGIS: QField Sync Plugin
Direct to Plugins > Manage and Install Plugins > All
Search for QFieldSync and install it
In QGIS a new toolbar should appear
Start QField Sync
Login to QFieldCloud with your username and password. If you have no username you can directly register following the link

## Slide 21
QField cloud
In QGIS: QField Sync Plugin
6. Click on Plugins > QFieldSync > QfieldCloud Projects Overview
7. In the QFieldCloud Projects Overview window, click on the Create new Project

## Slide 22
QField cloud
In QGIS: QField Sync Plugin
6. Click on Plugins > QFieldSync > QfieldCloud Projects Overview
7. Click on the Create new Project
8. Choose the recommended option and click Next
9. You can enter a description and click on Create and QFieldSync will package your project for the cloud

## Slide 23
QField cloud
In QField: Synchronise in the app
On your mobile device open QField Application
Click on QFieldCloud Projects and sign in with the same credentials as before
Your project should already be available
Click on it and download the project

## Slide 24
QField cloud
In QField: Synchronise in the app
On your mobile device open QField Application
Click on QFieldCloud Projects and sign in with the same credentials as before
Your project should already be available
Click on it and download the project
Now you can do field work!

## Slide 25
QField cloud
In QField: Synchronise back
Open the Side Dashboard:
Click on the blue cloud, the number indicates how many changes you have made)
Choose to push the changes if you are happy with your field work

## Slide 26
QField offline
In QGIS: Prepare your project
Create an offline copy of your QGIS project as a new file by adding “_offline.qgs” into a new folder

## Slide 27
QField offline
In QGIS: Layer packaging
Each layer needs a "Layer Action" to define how QFieldSync handles it
Available Action Types:
Copy: Creates static copy, no change tracking (for reference data)
Keep existing (copy if missing): Avoids re-packaging, best for frequent syncs
Offline editing: Full tracking with changelog, enables synchronisation (for the field)
Directly access data source: Real-time access (requires internet)
Remove: Excludes layer from mobile project

## Slide 28
QField offline
In QGIS: Layer packaging
Add the Google Satellite basemap
Zoom into your area of interest usingOSM Place Search
Toolbox > Raster tools > Generate XYZ tiles
Click Extent, select Draw on Map Canvas and draw AOI
Complete the dialog box as shown >
Save the file to the offline project folder created
Remove the Google Satellite basemap and add the saved MBTiles to the project

## Slide 29
QField offline
In QGIS: Package for QField
Go to Plugins > QFieldSync > Preference
Set the Default packaging import and export directory to the Import and Export Folders created on your local drive

## Slide 30
QField offline
In QGIS: Package for QField
Click on the MBTiles in your layers > Properties > QField
Change the Cable packing action to “Keep existent (Copy if missing)”
Repeat this change for the lulc_samples layer and any additional layer you may have
On the Toolbar, click on the Package for QField icon and confirm the packaged project directory
Click Create to complete

## Slide 31
QField offline
In QField: Manually synchronise
Copy the packaged folder into the qfield folder on your mobile device via USB, Mail, etc.
Open QField App on your mobile device
Select Open local file
Add your project by clicking on the green and white + icon at the bottom left
Select Import project from folder and navigate to the QField folder on your device
Now you can do field work!

## Slide 32
QField offline
In QField: Synchronise back
Once done with your collection, it is time to synchronise the data with your Desktop project:
Re-open the project in QGIS (the one you saved with a regular Save As) previously
Copy the project folder from your mobile device to the Import folder on your computer
Direct to Plugin > QFieldSync > Synchronise from QField menu to synchronise your changes from the QField project to the Desktop project

## Slide 33
QField bridges desktop GIS and field data collection
Proper QGIS project and layer configuration is essential for success
Two deployment options: Cloud (internet required) or offline
Data synchronisation preserves all attributes and geometries
Summary & key takeaways

## Slide 34
Sources
opengisch. (n.d.). QField for QGIS [GitHub repository]. Retrieved March 31, 2025, from https://github.com/opengisch/QField

## Slide 35: Thank you for your attention!
Dr. Insa Otte, Hanna Schulten
(on behalf of the EOCap4Africa Team)
and colleagues
insa.otte@uni-wuerzburg.de