## Slide 1
EOCap4Africa 5a Remote Sensing Data: Preprocessing

## Slide 2: Recap

## Slide 3
Active vs. passive remote sensing
Active sensor: emits EM energy and detects the energy returning from the object or surface
Passive sensors: measure solar or terrestrial energy
A remote sensor measures reflected or emitted energy. An active sensor has its own source of energy.
Tempfli et al., 2009
Notes: Principles of remote sensing : an introductory textbook.
January 2009
In book: Principles of Remote Sensing
Edition: ITC Educational Textbook Series 2,
Chapter: 2.2-2.4
Publisher: University of Twente Faculty of Geo-Information and Earth Observation (ITC),
Editors: Tempfli K, G.C. Huurneman, W.H. Bakker, and L.L.F. Janssen
Klaus Tempfli
G.C. Huurneman
Wim Bakker
Tsehaie Woldai

## Slide 4: Preprocessing of optical data

## Slide 5
The purpose of preprocessing satellite imagery
Raw satellite imagery inherits systematic error of various kinds
These systematic errors depend on the acquisition technique
These ‘unwanted’ effects can be of radiometric or spatial nature, meaning that the value that was recorded, does not relate to the actual ground observation or that the pixel we look at is distorted in some way
Using this as a basis for any kind of scientific analysis propagates errors, which can lead to misclassifications and wrong conclusions
Consequently, solely completely calibrated data allows to detect and precisely quantify trends of changes in land cover
Notes: https://byjus.com/physics/electromagnetic-waves/

## Slide 6
Factors influencing the RS image acquisition
Sensor characteristics (radiometry)
Weather, particular cloud cover
Earth surface (geometry)
Atmosphere
Acquisition method: satellite or airborne
Others
However, RS images should be comparable:
  In time (e.g., monitoring)
  Between sensors (e.g., MODIS and Landsat TM)
Notes: https://byjus.com/physics/electromagnetic-waves/

## Slide 7
Preprocessing of optical data
Processing Levels
With optical data sets, we can divide the data into what is called ‘processing levels’
This term describes how many different calibration and registration algorithms were performed on a certain data set
On the next slide, you can see the breakdown of the structure of Sentinel-2 data that is created by the European Space Agency (ESA). The structure is exemplary for other commonly used optical satellites

## Slide 8
Preprocessing of optical data
Processing Levels
Sentinel-2 Processing levels. (ESA 2021)
Notes: https://sentiwiki.copernicus.eu/web/s2-processing

## Slide 9
Preprocessing of optical data
Processing Levels – General Systematic:
Level 0: Raw data without any calibration or correction (not of interest for us)
Level 1A: Raw data bundled with radiometric and geometric calibration and correction coefficients as well as geolocation information, where radiometric correction deal with internal anomalies in detector sensitivity or detector noise and geometric corrections deal with image distortions, e.g., due to the optics of the sensor or the rotation of the Earth
Level 1B: Radiometric and geometric calibration and corrections from Level 1A have been applied to the raw data. Each pixel now corresponds to an explicit location on Earth – it is georeferenced. This is the minimum processing level you should strive for

## Slide 10
Preprocessing of optical data
Processing Levels – General Systematic:
Level 2: Geophysical parameters, such as reflectance at the Earth’s surface, land surface temperature or soil moisture, have been completed. The calculation of these parameters requires the application of various transformations and corrections, including, e.g., corrections for atmospheric scattering or surface properties
Level 3: Variables mapped on uniform space-time grid scales, usually with some completeness and consistency.
Level 3A: L3A data are generally periodic summaries (weekly, 10-days, monthly) of L2 products
Level 4: Model output or results from analyses of lower-level data (e.g., variables derived from multiple measurements)

## Slide 11
Striping
Due to non-identical detector response
  Detector characteristics
  Change with time / rise of temperature
  failure
Various methods (sometimes used in combination)
  Look up tables (radiometric response measurements at different brightness levels)
  Onboard calibration
  Histogram matching (gain and offset) – line pattern

## Slide 12
Striping
Comparison between Landsat 5 TM Band 1 difference images with different levels of calibrations and corrections applied. Bright areas in the lakes represent the point of no change. Most values are between - 50 (dark, Band 1 drop between 1997 and 1998 images) and + 20 digital numbers (DN) (bright, Band 1 gain between 1997 and 1998).
(Vogelmann et al. 2001)
Notes: Effects of Landsat 5 Thematic Mapper and Landsat 7 Enhanced Thematic Mapper Plus radiometric and geometric calibrations and corrections on landscape characterization
October 2001
Remote Sensing of Environment 78(1):55-70
DOI: 10.1016/S0034-4257(01)00249-8
Jim Vogelmann
Dennis Helder
Ron Morfitt
Henry Bulley

## Slide 13
(Partially) missing lines
Errors in
  Sampling or scanning equipment
  Transmission or recording of image data
  Reproduction of the media containing the data
Two methods
  Interpolations using data from adjacent scan lines
  Interpolation data at the same scan line from different spectral bands
Band gaps in Landsat 7 (EROS, 2025)
Notes: https://www.usgs.gov/landsat-missions/landsat-7
Eher: v

## Slide 14
Solar angle correction
Position of the sun relative to the earth changes depending on time of the day and the day of the year
In the northern hemisphere the solar elevation angle is smaller in winter than in summer
Sun elevation difference per season (adapted from Lillesand and Kiefer, 2015)
Notes: Remote Sensing and Image Interpretation
Lillesand, Thomas / Kiefer, Ralph W. / Chipman, Jonathan
7. Auflage März 2015 768 Seiten, Softcover Lehrbuch
ISBN: 978-1-118-34328-9
John Wiley & Sons

## Slide 15
Solar angle correction
An absolute correction involves dividing the DN-value in the image data by the sine of the solar elevation angle
Size of the angle is given in the header of the image data

## Slide 16
Solar irradiation correction
Scene illumination
Position of sun
  Sun elevation (sun-angle)
  Sun- earth distance
Correction elevation
  Normalization
  Division of each pixel value by the sine of solar elevation angle for particular time and location per spectral band
Correction distance
  Sun irradiance decreases with square of distance
  normalization
Sun elevation difference per season (adapted from Lillesand and Kiefer, 2015)
Notes: Remote Sensing and Image Interpretation
Lillesand, Thomas / Kiefer, Ralph W. / Chipman, Jonathan
7. Auflage März 2015 768 Seiten, Softcover Lehrbuch
ISBN: 978-1-118-34328-9
John Wiley & Sons

## Slide 17
Radiometric calibration
Sensor calibration before launch:
From DN to physical units
Pre-launch calibration
Correction factors for all channels:
  Bias (A0)
  Gain (A1)
L = A0 + A1 *DN
  L = spectral radiance
  DN = digital number
MERIS pre-launch calibration in lab. (ESA, 2025)
Response function for a TM band
Notes: https://earth.esa.int/eogateway/instruments/meris/description

## Slide 18
Sensor calibration
Necessary to generate absolute data on physical properties
  Reflectance
  Temperature
  Emissivity
  Backscatter
Values provided by data provider / agency

## Slide 19
Value conversion
The conversion from DN to radiance and reflectance is an important step in the preprocessing
In case of Sentinel-2 and Landsat data, we are usually interested in the bottom-of-atmosphere (BOA) reflectance, which is, in contrast to the top-of-atmosphere (TOA) reflectance, corrected for atmospheric impacts and can thus directly be interpreted
However, the initially available data sets are being converted from DN to TOA format
For the conversion, the data is rescaled using sensor specific equations containing information about sun-related angles and other parameters

## Slide 20
Value conversion
An example for such a conversion, the expression used to correct Landsat 8 OLI data is given below:
By using these equations, we can compute TOA values which are subject to strong illumination geometry difference-related effects and therefore should not be favored over BOA reflectances
Notes: https://www.usgs.gov/landsat-missions/landsat-8-oli-and-tirs-calibration-notices

## Slide 21
Terrain effects
Cause differential solar illumination
  Some slopes receive more sunlight than others
Magnitude of reflected radiance reaching the sensor
  Topographic slope and aspect
  Bidirectional reflectance distribution function (BRDF)

## Slide 22
Terrain effects
Minnaert correction
  First order correction for terrain illumination effects
  Ln = L * cos(e)k-1 * cos(i)k
  Ln - normalized radiance
  L - measured radiance
  e - slope (derived from DEM)
  i - incidence angle of solar radiation
  k - Minnaert constant (estimated for each image)

## Slide 23
Terrain effects
Shaded relief model (SRM)
  Requires digital elevation model
  Generated with constant albedo (brightness dependent solely on topographic effects)
  Ratio of image and SRM yields spectral radiance of ground cover (noisy)
  Alternative:
  DNcorr = m * (DN – SRMDN) + a

## Slide 24
Atmospheric correction – why?
Physical relation of radiance to surface property
  Atmospheric component needs to be removed
Multispectral data for visual analysis
  Scattering increases inversely with wavelength
Image ratios
  Leads to biased estimate
Time difference between image acquisition and ground truth measurements

## Slide 25
Atmosphere and radiation
Relationship between radiance received at the sensor (above atmosphere) and radiance leaving the ground
Ls = H * ρ * T + Lp
  Ls - at sensor radiance
  H - total downwelling of target
  ρ - reflectance of target
  T - atmospheric transmittance
  Lp - atmospheric path radiance (wavelength dependent)

## Slide 26
Atmospheric correction methods
Image-based methods
  Histogram minimum method
  Regression method
Radiative transfer models
Empirical line method

## Slide 27
Atmospheric correction methods
Histogram minimum method
Histograms of pixel values in all bands
Pixel values of low reflectance areas near zero
  Exposure of dark colored rocks
  Deep shadows
  Clear water
Lowest pixel values in visible and near-infrared are approximation to atmospheric path radiance
Minimum values subtracted from image

## Slide 28
Atmospheric correction methods
Regression method
Applicable to dark pixel areas
Near-infrared pixel values are plotted against values in other bands
Least square line fit using standard regression methods
Resulting offset is approximation for atmospheric path radiance
Offset subtracted from image

## Slide 29
Atmospheric correction methods
Radiative transfer models
Limited by the need to supply data about atmospheric conditions at time of acquisition
Mostly used with “standard atmospheres”
Available numerical models
  LOWTRAN 7
  MODTRAN 4
  ATREM
  ATCOR
  6S (Second Simulation of the Satellite Signal in the Solar Spectrum)

## Slide 30
Atmospheric correction methods
Empirical line method
Selection of one dark and one bright target
Ground reflectance measurement
  Field radiometer
Sensor radiance computed from image
Slope s = cos (α) and intercept a of line joining two targets
Gens, 2024
Notes: Rüdiger Gens (2024) Atmospheric and Radiometric Corrections for Remote Sensing Data. Geophysical Institute. University of Alaska Fairbanks

## Slide 31
Atmospheric correction methods
Haze
Due to Rayleigh scattering
  Particles size responsible for effects smaller than the radiation‘s wavelength (e.g., oxygen and nitrogen)
Haze has an additive effect resulting in higher DN values
Decreases the general contrast of the image
Effect is wavelength dependent
  More pronounced in shorter wavelengths and negligible in the NIR

## Slide 32
Atmospheric correction methods
Haze

## Slide 33
Influence of Cloud Cover
Cloud cover is a common problem in optical remote sensing images due to its contamination of the reflectance from the Earth’s surface
Cloud removal has become a necessary preprocessing step for most applications
Cloud cover may render an optical remote sensing image useless
ASTER satellite, north of the Netherlands

## Slide 34
Influence of Cloud Cover
Pathway A: direct reflected sunlight
Pathway B: skylight
Pathway C: air light
Atmospheric influence in two directions (up and down)
Generalized overview of pathways from sun to remote sensing sensor

## Slide 35
Histogram stretching
Stretching of digital numbers (rescaling over the range of the greyscale histogram) to allow better visibility and pixel distinction.
(EOcollege, 2025)
Notes: https://eo-college.org/courses/landinfocus/lessons/processing-fundamentals-of-remote-sensing-imagery/topics/preprocessing-sar-and-optical/

## Slide 36
Remove spatial distortion
Geometric correction to remove spatial distortions. This process corrects the discrepancy between an image coordinate and the actual position on the Earth’s surface. Exemplary, this can be done using ground control points (GCPs) from known ‘correct’ images.
(EOcollege, 2025)
Notes: https://eo-college.org/courses/landinfocus/lessons/processing-fundamentals-of-remote-sensing-imagery/topics/preprocessing-sar-and-optical/

## Slide 37
Low pass filtering
Low pass filtering to smoothen satellite imagery using moving window (e.g., 3 x 3 pixels), which are used to calculate local averages for kernel pixels.
(EOcollege, 2025)
Notes: https://eo-college.org/courses/landinfocus/lessons/processing-fundamentals-of-remote-sensing-imagery/topics/preprocessing-sar-and-optical/

## Slide 38
High pass filtering
High pass filtering to sharpen edges and increasing contrast. They enhance spatial frequencies / components (e.g., edges). Subtracts the low pass filter from the original image.
(EOcollege, 2025)
Notes: https://eo-college.org/courses/landinfocus/lessons/processing-fundamentals-of-remote-sensing-imagery/topics/preprocessing-sar-and-optical/

## Slide 39: Sensor Accuracy

## Slide 40
Sensor Accuracy
General Accuracy Assessment
Principles of Validation
Remote Sensing is an indirect technique to measure or quantify the studied objects 🡪 Errors during the estimation process are inevitable.
Error assessment or validation is typically performed regarding an independent measurement of the target quantity – e.g., the measurement was taken with another instrument or by applying another, more robust method.
Usually, these validation measurements are also expected to have a higher quality than the RS derived estimates 🡪 Ground truth is used to talk about these measurements.

## Slide 41
Sensor Accuracy
General Accuracy Assessment
Accuracy and precision
Relate to quality
Accuracy
Refers to distance of a measure (or prediction) to the true value
Can be referred to as trueness
An accurate measurement produces results that are close to the true value

## Slide 42
Sensor Accuracy
General Accuracy Assessment
Accuracy and precision
Relate to quality
Precision
Refers to repeatability or reproducibility of a measurement
Refers to the spread that occurs if the measurement (or prediction) is repeated under the same conditions
A precise measurement produces results that are close to each other, no matter their distance from the true value

## Slide 43
Sensor Accuracy
General Accuracy Assessment
Quality metrics
For validation purposes, many quality indicators or metrics exist 🡪 meant to make the error assessment quantifiable and objective
They are used in scientific publications and reports to allow comparing different RS products with each other.
The error metric that should be used to assess the quality of a RS product depends first on its type: interval and ratio scale variables like reflectance or Leaf Area Index require different metrics than nominal and ordinal scale variables like land cover.
Error assessment for nominal and ordinal scale variables, important for land cover, are discussed in the classification topic.

## Slide 44
Sensor Accuracy
General Accuracy Assessment
Quality metrics – R-squared
R-squared is a measure of how well a linear regression model fits the data. It can be integrated as the proportion of variance of the outcome Y explained by the linear regression model.
It is a number between 0 and 1 (0 ≤ R² ≤ 1). The closer its values is to 1, the more variability the model explains. And R² = 0 means that the model cannot explain any variability in the outcome Y.

## Slide 45
Sensor Accuracy
General Accuracy Assessment
Quality metrics – R
On the other hand, the correlation coefficient r is a measure that quantifies the strength of the linear relationship between 2 variables.
r is a number between -1 and 1 (-1 ≤ r ≤ 1):
A value of r close to -1: means that there is negative correlation between the variables (when one increases the other decreases and vice versa)
A value of r close to 0: indicates that the 2 variables are not correlated (no linear relationship exists between them)
A value of r close to 1: indicates a positive linear relationship between the 2 variables (when one increases, the other does)

## Slide 46
Sensor Accuracy
General Accuracy Assessment
Quality metrics – Root Mean Square Error (RMSE)
RMSE measures the accuracy of an RS product, i.e., the distance of RS predictions from the corresponding ground truth measurements. It is defined as:
It should be used when comparing metrics that should by definition be the same quantities, e.g., if Leaf Area Index (LAI in m2/m2) is derived from RS data, it can be compared to ground truth LAI data with the RMSE.
has the same physical unit as the RS product and the ground truth. It should be noted that the RMSE weights large errors heavier than smaller errors because of the square. Also, positive (overestimation) and negative (underestimation) errors have the same impact on RMSE.

## Slide 47
Sensor Accuracy
General Accuracy Assessment
Quality metrics – Mean Absolute Error (MAE)
MAE measures the average magnitude of the errors in a set of predictions
Is not considering their directions
It is the average over the test sample of the absolute differences between prediction and actual observation where all individual differences have equal weight

## Slide 48
Sensor Accuracy
Surface Reflectance
Surface reflectance is a basic product in remote sensing and starting point for many applications
Still, there are several error sources contributing to the “measured” surface reflectance
  Sensor calibration
  Atmospheric correction

## Slide 49: Thank you for your attention!
Dr. Insa Otte (on behalf of the EOCap4Africa Team) and colleagues
insa.otte@uni-wuerzburg.de

## Slide 50
References
EOcollege. (n.d.). Land in Focus – Basics of Remote Sensing. Retrieved 3 February 2026, from https://eo-college.org/courses/landinfocus/
EROS. (n.d.). Dolan Springs, Arizona. Retrieved https://eros.usgs.gov/media-gallery/image-of-the-week/dolan-springs-arizona
ESA. (n.d.-a). MERIS Overview. Retrieved 3 February 2026, from https://earth.esa.int/eogateway/instruments/meris/description
ESA. (n.d.-b). S2 Processing. Retrieved https://sentiwiki.copernicus.eu/web/s2-processing
Gens, R. (n.d.). Atmospheric and Radiometric Corrections for Remote Sensing Data. Retrieved 3 February 2026, from https://rudigens.github.io/asf_seminar/corrections.pdf
Lillesand, T., Ralph|Chipman, Jonathan. (2004). Remote Sensing and Image Interpretation. Wiley-Blackwell.
Tempfli, K., Huurneman, G. C., Bakker, W. H., Janssen, L. L. F., Feringa, W. F., Gieske, A. S. M., Grabmaier, K. A., Hecker, C. A., & Horn, J. A. van der (Eds). (2009). Principles of remote sensing: An introductory textbook (Fourth edition). ITC.
USGS. (n.d.). Landsat 8 OLI and TIRS Calibration Notices. Retrieved 3 February 2026, from https://www.usgs.gov/landsat-missions/landsat-8-oli-and-tirs-calibration-notices
Vogelmann, J. E., Helder, D., Morfitt, R., Choate, M. J., Merchant, J. W., & Bulley, H. (2001). Effects of Landsat 5 Thematic Mapper and Landsat 7 Enhanced Thematic Mapper Plus radiometric and geometric calibrations and corrections on landscape characterization. Remote Sensing of Environment, 78(1–2), 55–70. https://doi.org/10.1016/S0034-4257(01)00249-8