## Slide 1
EOCap4Africa 4 Coordinate Reference Systems and Projections

## Slide 2: Coordinate Reference Systems

## Slide 3
Geoid
The “blue marble” – or is marble really the right term?
NASA, 2000
Notes: http://antwrp.gsfc.nasa.gov/apod/image/0304/bluemarble2k_big.jpg bild verweist auf ein anderes Bild

## Slide 4
Geoid
What is the shape of the Earth?
The Geoid (scale factor: 1000). Wikimedia Commons, 2022
Notes: https://commons.wikimedia.org/wiki/File:Geoid_undulation_10k_scale.jpg
Eher: https://essd.copernicus.org/articles/11/647/2019/

## Slide 5
Geographic Coordinate System
The Earth’s Geographic Coordinate System: unlike cartesian systems it is not planar, but spherical and uses angles (latitudes and longitudes) to describe locations. Wikimedia Commons, 2022
Notes: https://prixa.com.np/geographic-coordinate-system/

## Slide 6
Geographic Coordinate System
Localization on Earth:
Geoid: geometric shape of the Earth 🡪 approximated as a rotating sphere (ellipsoid)
Geographic Coordinate System:
  Latitude: angle between perpendicular of rotating sphere and equatorial plane at point on sphere
  Longitude: angle between prime meridian and a plane through North and South pole at point on sphere
Equatorial plane: simply derivable from the axis of rotation (natural)
Prime Meridian: artificially defined, Eastern and Western hemisphere

## Slide 7
Geographic Coordinate System
The Geographic Coordinate System is using 360 longitudes and 180 latitudes and uses the following systems:
DD: Decimal Degrees (29.1000°, -113.3000°)
DM: Degrees Decimal Minutes (39°33.0’, -125°31.0)
DMS: Degrees Minutes Seconds (39°23’05’’N, 113°27’01’’W)

## Slide 8: What is a projection?

## Slide 9
Projecting
Projecting a spherical surface onto a plane. (Neteler and Mitasova 2008)
Notes: Neteler and Mitasova, 2008
M. Neteler, H. Mitasova
Open Source GIS: A GRASS GIS Approach (Third edition), Springer, NY (2008), p. 406
Cite this chapter
(2005). Satellite Image Processing. In: Open Source GIS: A Grass GIS Approach. The International Series in Engineering and Computer Science, vol 773. Springer, Boston, MA. https://doi.org/10.1007/1-4020-8065-4_9

## Slide 10
Projecting - Distortions
Distortions visualized for the often-used Mercator projection: Direction and shapes are correct, but area and distance are distorted.
(Wikimedia Commons, 2022)

## Slide 11
Projecting
Projecting Earth’s spherical surface onto a plane:
Projection: Transfer of the 3D-shape of the Earth’s surface onto a 2D-plane (e.g., a map) 🡪 non-trivial mathematical problem
Projected coordinate system: Points to locations on a plane
Geometry: There are four fundamental geometric properties to any geometric feature on a sphere: (i) area, (ii) distance, (iii) direction and (iv) shape
Distortions: only two of these four can be preserved by a single projection 🡪 mathematical constraint

## Slide 12
Projecting – why?
Projections allow you to work with spherical data on a cartesian-like grid with dimensions and units easy to interpret
Earth observation and other spatial data are delivered projected, and you need to be able to deal with their projection
If you use data from different sources, you need to be able to reproject them to a uniform projection
Thus, you need to be able to decide which projection to use for your project
You might need to project unprojected (geographical, spherical) data to jointly analyze them with projected data

## Slide 13
Projecting – What kind of projections exist?
Conformal: map projections preserving angles locally and thereby shape
Equal-Area: map projections preserving area
Equidistant: map projections preserving distance
True direction: map projections preserving direction

## Slide 14
Projecting – Different ways
Cylindrical
Azimuthal (planar)
(USGS Projection Map, 2023)
(USGS Projection Map, 1993)
Notes: Projection Methods
A projection method is a mathematical formula that converts spherical data (3D) into rectangular (2D) data. This formula can then have settings that change the position of the projection on the globe.
The graphics below are taken from the USGS Projection Map (USGS Projection Map). This is an excellent resource for information on commonly used projection methods.
Cylindrical Projection Methods
Mercator
Notice in the Mercator projection method that it; is a cylindrical projection, touches at the equator and has a setting for the Central Meridian. Because it touches at the equator, the distortion near the equator is small but the distortion increases rapidly as you move away from the equator.
Azimuthal (Planar)
Azimuthal projection methods project geographic data onto a plane. They are typically used to represent data at the poles.
Orthographic
The orthographic projection is a special azimuthal projection that makes it look like we are looking at the earth in a photo graph. GoogleEarth uses this projection. Take a minute and examine the graphic and think about where the distortion is high and where it is low.
For information on USGS data, maps, products, publications,
and services, call 1-888-ASK-USGS (1-888-275-8747), or visit
the USGS Publications and Other Products website at:
http://www.usgs.gov/pubprod/.
Please visit the Ask USGS website at http://ask.usgs.gov/ or
the USGS home page at http://www.usgs.gov/.
U.S. Department of the Interior
U.S. Geological Survey

## Slide 15
Projecting – Different ways
Conic
Polyconic
(USGS Projection Map, 2023)
(USGS Projection Map, 1993)

## Slide 16
Albers Conic Equal Area (created by GMT)
Conic Projections
Albers Conic Equal Area Projection
Used to map regions of large east-west extent
More closely spaced at the north edge of the map
Projection is equal area
Notes: https://docs.generic-mapping-tools.org/6.6/reference/map-projections.html

## Slide 17
Lambert Conic Conformal (created by GMT)
Conic Projections
Lambert Conic Conformal Projection
Similar to the Albers projection to map regions of large east-west content
Unlike the Albers projection, Lambert’s conformal projection is not equal-area
Notes: https://docs.generic-mapping-tools.org/6.6/reference/map-projections.html

## Slide 18
Conic Projections
Equidistant Conic Projection
Neither conformal or equal-area, but serves as a compromise between them
Equidistant Conic (created by GMT)
Notes: https://docs.generic-mapping-tools.org/6.6/reference/map-projections.html

## Slide 19
Azimuthal Projections
Lambert Azimuthal Equal Area Projection
Developed in 1772 by Lambert
Used for mapping large regions (e.g., continents)
It is an azimuthal, equal-area projection but not perspective
Lambert Azimuthal Equal Area (created by GMT)
Notes: https://docs.generic-mapping-tools.org/6.6/reference/map-projections.html

## Slide 20
Azimuthal Projections
Polar Stereographic Conformal (created by GMT)
Polar Stereographic Conformal Projection
Conformal and azimuthal
Dates back to the Greeks
Main use for mapping polar regions
Notes: https://docs.generic-mapping-tools.org/6.6/reference/map-projections.html

## Slide 21
Azimuthal Projections
Orthographic Projection
Perspective from an infinite distance
Used for appearance of the earth from space
Much distortion is introduced
Orthographic (created by GMT)
Notes: https://docs.generic-mapping-tools.org/6.6/reference/map-projections.html

## Slide 22
Azimuthal Projections
Equidistant Azimuthal Projection
Direction from the center is true
Several centuries old
Equidistant Azimuthal (created by GMT)
Notes: https://docs.generic-mapping-tools.org/6.6/reference/map-projections.html

## Slide 23
Azimuthal Projections
Perspective Projection
Used for a 3D appearance on a 2D plane
Perspective (created by GMT)
Notes: https://docs.generic-mapping-tools.org/6.6/reference/map-projections.html

## Slide 24
Cylindrical Projections
Mercator Projection
Probably most famous
Originated from G. Cremer (Flemish cartographer, 1569)
Cylindrical and conformal, no distortion along equator
Distortion towards poles larger (e.g., Greenland larger than S-America
Mercator (created by GMT)
Notes: https://docs.generic-mapping-tools.org/6.6/reference/map-projections.html

## Slide 25
Cylindrical Projections
Mercator (USGS)
Notes: https://docs.generic-mapping-tools.org/6.6/reference/map-projections.html

## Slide 26
Cylindrical Projections
Transverse Mercator Projection
Lambert 1772
Distortion increases away from the central meridian
Transverse Mercator (created by GMT)
Notes: https://docs.generic-mapping-tools.org/6.6/reference/map-projections.html

## Slide 27
Cylindrical Projections
Transverse Mercator Projection
Lambert 1772
Distortion increases away from the central meridian
Transverse Mercator (USGS)
Notes: https://docs.generic-mapping-tools.org/6.6/reference/map-projections.html

## Slide 28
Cylindrical Projections
Universal Transverse Mercator Projection
Subset of the Transverse Mercator Projection
Adopted by the US Army for maps
Globe divided into 60 zones (84S-84N)
Each UTM zone has unique central meridian
Universal Transverse Mercator (created by GMT)
Notes: https://docs.generic-mapping-tools.org/6.6/reference/map-projections.html

## Slide 29
Cylindrical Projections
Universal Transverse Mercator Projection
Subset of the Transverse Mercator Projection
Adopted by the US Army for maps
Globe divided into 60 zones (84S-84N)
Each UTM zone has unique central meridian
UTM zones of Africa: Map of Africa, showing the latitude and longitude zones of the en:Universal Transverse Mercator coordinate system, from 28H to 39S.
Wikimedia Commons, 2022

## Slide 30
Projections
Projection characteristics:
Groups: conformal (true shape/angle), equal-area (true area), equidistant (true distances), true direction
Types: Cylindrical, Azimuthal (planar), Conic, Polyconic
No perfection, every projection is distorted
Different projections are suitable for different applications and geographic areas/extents

## Slide 31: Coordinate Reference System

## Slide 32
Terminology – Geographic Coordinates vs. CRS
It is important to know the difference between the following terms (even though they sound all so similar):
Geographic Coordinate System: Not a projection, but the spherical coordinate system of the Earth
Coordinate Reference System (CRS): Describes a projection, transforming spherical data (3D) into a planar system (2D)
A CRS consists of:
Geodetic datum, the geodetic reference system: placing reference locations on the Earth’s sphere and thereby defines the ellipsoid approximating the sphere and how it is placed (e.g., the popular WGS84)
Coordinate System: projecting a coordinate grid of some sort onto the geodetic reference system
Units: spatial measure used by the CRS, e.g., meters, feets, degrees

## Slide 33
Which CRS should I use?
Global Scale: e.g., Sinusoidal Equal Area
Continental Scale: e.g., Lambert Azimuthal Equal Area
Small Scale: e.g., Universal Transverse Mercator (UTM) with WGS84, Lambert Conformal Conic

## Slide 34
Which CRS should I use?
Choice depends on:
Your aim: Where is your research area) How large does it spread? Which attributes do you want to preserve/distort?
Your data: With which CRS are your data delivered? Is it worth transforming them? Which common CRS for all your data imposes the least added inaccuracies?
Your project partners: With which CRS are they working? What CRS should your project be delivered in, e.g., to ease interpretability?

## Slide 35
CRS – Implementation example I
Human-readable CRS designation: Universal Transverse Mercator (UTM) World Geodetic System 1984 (WGS84) Zone 32N
Authority ID: EPSG: 32632
Proj4 string:

## Slide 36
CRS – Implementation example II
Well-known text (WKT):

## Slide 37
CRS – Implementation example III

## Slide 38
CRS and coordinates
Original coordinates and matching CRS

## Slide 39
CRS and coordinates
Reprojecting (transforming, warping)
Coordinate grid is recalculated based on new CRS, both coordinates and CRS change

## Slide 40
CRS and coordinates
Assigning a new CRS
Coordinates are not changes, new CRS is assigned, coordinates and CRS do not match anymore

## Slide 41: Thank you for your attention!
Dr. Insa Otte (on behalf of the EOCap4Africa Team) and colleagues
insa.otte@uni-wuerzburg.de

## Slide 42
Recourses
Burlakoti, N. (n.d.). Geographic Coordinate System. Retrieved 3 February 2026, from https://prixa.com.np/geographic-coordinate-system/
GMT. (n.d.). GMT Map Projections. Retrieved 3 February 2026, from https://docs.generic-mapping-tools.org/6.6/reference/map-projections.html
Ince, E. S., Barthelmes, F., Reißland, S., Elger, K., Förste, C., Flechtner, F., & Schuh, H. (2019). ICGEM – 15 years of successful collection and distribution of global gravitational models, associated services, and future plans. Earth System Science Data, 11(2), 647–674. https://doi.org/10.5194/essd-11-647-2019
NASA. (n.d.). Bluemarble2k. Retrieved 3 February 2026, from https://apod.nasa.gov/apod/image/0304/bluemarble2k_big.jpg
Neteler, M., & Mitasova, H. (2004). Satellite Image Processing. In Open Source GIS: A Grass GIS Approach (Vol. 773, pp. 201–252). Springer US. https://doi.org/10.1007/1-4020-8065-4_9
USGS. (1993). Map Projections. https://doi.org/10.3133/70047422